## Slide 1: ME469: Review of Partial Differential Equations
Stefan P. Domino1,2
1 Computational Thermal and Fluid Mechanics, Sandia National Laboratories
2 Institute for Computational and Mathematical Engineering, Stanford
SAND2018-4536 PE

## Slide 2: Equation Review
The intended application
Physical laws, hypothesis and models (e.g. a set of PDEs) and initial and boundary conditions
A set of computational algorithms that allow to build a numerical, or approximated solution to the conceptual model
Real World
Conceptual
Model
Computer Model

## Slide 3: Partial Differential Equation: Transient Evolution of a Scalar with Advection, Diffusion, and Source
General Transport Equation using Einstein notation, i.e., repeated index, for scalar f
Density, r [kg/m3]
Velocity, uj [m/s]
Mass diffusivity, D [m2/s2]
Dynamic viscosity, m [kg/(m-s)]
Schmidt number, Sc
Time term, or “accumulation”
advection
diffusion
source/sink term
Repeated Index Example

## Slide 4: Partial Differential Equation: Transient Evolution of a Scalar with Advection
General Transport Equation using Einstein notation, i.e., repeated index, for scalar f
Density, r [kg/m3]
Velocity, uj [m/s]
Mass diffusivity, D [m2/s2]
Dynamic viscosity, m [kg/(m-s)]
Schmidt number, Sc
0.0
0.0
Dt
ux

## Slide 5: Partial Differential Equation: Transient Evolution of a Scalar with Diffusion
General Transport Equation using Einstein notation, i.e., repeated index, for scalar f
Density, r [kg/m3]
Velocity, uj [m/s]
Mass diffusivity, D [m2/s2]
Dynamic viscosity, m [kg/(m-s)]
Schmidt number, Sc
0.0
0.0
Dt

## Slide 6: Partial Differential Equation: Transient Heat Conduction
Thermal Heat Conduction
Density, r [kg/m3]
Specific Heat, Cp [J/(kg-K)]
Thermal conductivity, l [W/(m-K)], 1W = 1 J/s
Heat flux vector, qj
Thermal heat conduction (outer shell heated)

## Slide 7: Variable Density, non-Isothermal Fluid Flow System
Consider the variable density (non-isothermal) equations of motion (momentum and continuity) with energy transport:
Equation of State (EOS) provides the P and r relationship
(2+nDim)
Constitutive Relationships

## Slide 8: Conserved vs Non-conserved Form
For the so-called non-conserved form, chain-rule the advection term, while enforcing continuity:
0.0

## Slide 9: Incompressible Navier Stokes
For a constant density and viscosity (in absence of a source term), we revert to the classic form:
0.0
0.0
(trick)
0.0